G-BNYB PA-28-201T 1979

# TAKE OFF AND CLIMB – DO NOT EXCEED 41” Hg of Manifold Pressure

Vr = 55 - 58 KIAS, Vy = 90 KIAS	Cruise climb 33”MP/2400 RPM 104 KIAS

Vr = 55 - 58 KIAS, Vx = 75 KIAS	Obstacle clearance with two notches of flap (25 ()

Soft and short field use 25 ( flap	Demonstrated crosswind is 20 kt.

# FUEL

75% Power 33.8”MP/2400 RPM @ 2500’ with mixture set to 12 USGPH 135 KIAS.

65% Power 29.0”MP/2300 RPM @ 2500’ with mixture set to 9.2 USGPH 120 KIAS.

Usable fuel is 72 US Gallons.

Aircraft weighs 1730 lb; usable fuel weighs 432 lb, leaving 738 lb for crew, passengers and baggage.

# APPROACH SPEEDS

Base trim to 85 KIAS with 25( flap.

Trim 74 KIAS with 40( of flap for a short field landing.

# STALLING SPEEDS

At 2900 lbs:	Vs1 = 67 KIAS (clean)	Vs0 = 59 KIAS (flaps 40().

# GLIDE

At 95 KIAS the aircraft will glide 4.1 nautical miles from 2 000’ agl.

# SUCTION

5 ( 0.1 inches of mercury	www.gridline.co.uk		7-Aug-05 G-BNYB.doc