### TSIO-360-F, -FB	Type Certificate E9CE

The TSIO-360-F, -FB engine is an air cooled turbocharged fuel injected engine producing 200 brake horsepower at a maximum crankshaft speed of 2575 RPM.  The engine has horizontally opposed air cooled cylinders.  The engine cylinders are cross flow design having overhead inclined valves.  The cylinders have downdraft intake inlets mounted on the top of the cylinder head and downdraft exhaust outlets located on the bottom of the cylinder.

The TSIO-360-F, -FB engines have a 360 cubic inch displacement achieved by using a cylinder design with a 4.438 inch diameter bore and a 3.875 inch stroke.  The dry weight of the engine is 328.35 lbs. without accessories.  The average weight of the engine with accessories is approximately 392 pounds.

| OVERALL ENGINE DIMENSIONS INCHES |
| --- |
| HEIGHT |  |
| WIDTH | 31.38 |
| LENGTH | 40.53 |

ENGINE SPECIFICATIONS	TSIO-360-F & -FB

Cylinders

Arrangement	Horizontally Opposed

Number of Cylinders	6

Compression Ratio	7.5:1

Firing Order	1-6-3-2-5-4

Bore (Inches)	4.438

Stroke (Inches)	3.875

Piston Displacement (cu. in.)	360

Brake Horsepower @ Rated Speed

Rated Maximum Continuous Operation	200 BHP @ 2575 RPM

Recommended Cruise	150 BHP @ 2450 RPM

OPERATING LIMITS

Manifold Pressure Limit (In. Hg.) Absolute	41.0”

Fuel Control System	TCM Fuel Injection

Fuel		100/100LL

Oil

| TEMPERATURE | AVIATION GRADE | SAE GRADE | MULTI-VISCOSITY |
| --- | --- | --- | --- |
| BELOW 40 | 65 | 30 | 10W-30 / 15W-50 / 20W-50 |
| ABOVE 40 | 100 | 50 | 15W-50 / 20W-50 / 20W-60 |

Oil Pressure

Idle, Minimum, psi	10

Normal Operation, psi	30-80

Oil Sump Capacity (U.S. Quarts)	8

Max. Oil Consumption (Lb./BHP/Hr. Max.)	   .006 X % Power

100

Oil Temperature Limits

Minimum for Take-Off	100( F

Maximum Allowable	240( F

Cylinder Head Temperature

Recommended Max. at Cruise	240( - 440( F

Limit	460( F

Turbine Inlet Temperature

Maximum Continuous	1725( F

Maximum, 60 Seconds	Not Applicable

Ignition Timing (Compression Stroke, Breaker Opens)

Right Magneto, Degrees BTC	20(

Left Magneto, Degrees BTC	20(

Spark Plug

TCM	630049

Champion	RHM38E