G-CKYL C42B 2018

# TAKE OFF AND CLIMB

Normal, Vr  is 41 kts, Vy is 64 kts with first stage flap.

Best angle climb speed Vx is 50 kts with first stage flap. This is not recommended due to potential loss of control in the event of an engine failure after take-off.

En route climb speed is 68 kts.

# FUEL

12.7 l/h @ 4600 rpm power cruise is 90 kts.

Usable fuel is 65 litres.

Aircraft weighs 288 kg, full fuel weighs 47 kg, leaving 137.5 kg for crew and baggage.

# APPROACH SPEEDS

Reduce power on base leg and trim to maintain 65 kts - top of white arc.  Apply first stage flap and simultaneously lower nose and trim to maintain 61 kts according to aim point on runway. Fly at 56 kts with full flap on short final when landing is fully assured.

Maximum wind speed in gusting conditions is 22 kts.

# UPPER AIR WORK

Stalls and steep turns (aerobatics and manoeuvres banking above 60 ( are prohibited).

# STALLING SPEEDS

Clean – Vs1  is 43 kts, first stage flap  15 (  - Vs2  is 38 kts, full flap 40 ( - Vs0  is 34 kts.

# GLIDE

At 58 kts the aircraft will glide 4 nautical miles from 2 000’ agl.

www.gridline.co.uk		22-Oct-23 G-CKYL.doc