Ex. 21 – HALF CUBAN 8

AIM: To fly ⅝ of a loop and as the aircraft is approaching the 45º nose down inverted attitude commence a half roll bringing the aircraft back to normal erect flight.

AIRMANSHIP: Lookout, HASELL

FLIGHT EXERCISE

(1) Safety checks completed and area cleared. Select a reference line feature. Position the aircraft and have a final lookout. The manoeuvre is started with the commencement of a normal loop.

(2) Ensure the reference line is maintained throughout the looping section.

(3) As the 45º nose down inverted position is approached, apply forward pressure on the control column and commence the roll, retarding the throttle as necessary.

(4) Continue the roll to the erect position whilst maintaining the reference line at a 45º downward angle.

(5) When the roll is completed, ease the aircraft up into the level flight attitude.