Ex. 21 – THE AILERON ROLL

AIM: To fly a 360 ( roll about the longitudinal axis by using all three controls with ailerons being considered as the primary control throughout.

AIRMANSHIP: Lookout, HASELL

FLIGHT EXERCISE:

(1) Safety checks completed and area cleared. Select a reference point. Final lookout.

(2) At 108 Kt raise the nose above the reference point in a positive manner. Following this a brief check forward on the control column to freeze the selected pitch attitude. Commence the roll by using aileron and rudder. As the airspeed decreases more deflection of the ailerons and rudder will be progressively required.

(3) By the time the aircraft reaches the inverted position apply full aileron and add some rudder to maintain the rate of roll. It will be essential not to apply any back pressure on the control column at this stage.

(4) During the roll from the inverted position to the three-quarter stage of the manoeuvre the ailerons will still have to be fully deflected.

(5) As the aircraft approaches the erect position all the controls are used in the normal manner to return the aircraft to straight and level flight.