Ex. 21 – SNAP ROLL

AIM: To fly a “spin” in a horizontal direction.

AIRMANSHIP: Lookout, HASELL

FLIGHT EXERCISE

(1) Select a reference point on or near the horizon. Complete the safety checks and ensure that no other aircraft are in the vicinity.

(2) Select the recommended power and raise the nose as necessary to obtain 81 – 86 Kt.

(3) When the recommended entry speed is achieved sharply apply full left rudder and bring the control column back to its limit.

(4) When the aircraft has rolled through approximately 270º, apply full opposite rudder and move the control column sharply forward to break the stall. At this stage the rotation will cease.

(5) Use all three controls to adjust the flight attitude for straight and level flight.