G-BACP FA-150L 1974

# TAKE OFF AND CLIMB

Vr = 60 mph, Vy = 78 mph	Normal take off

Vr = 60 mph, Vx = 70 mph	Short field with flaps up

Soft field use 10 ( flaps	Normal climb 75 - 85 mph.

# FUEL

4.9 USGPH @ 2450 RPM @ 2500’ with mixture leaned to max RPM – 103 mph TAS.

5.8 USGPH @ 2650 RPM @ 5000’ with mixture leaned to max RPM – 113 mph TAS.

Usable fuel capacity is 22.5 US Gallons.

Aircraft weighs 1 155 lb, full fuel weighs 135 lb, leaving 310 lb for crew.

# APPROACH SPEEDS

70 - 80 mph with flaps up, 60 - 70mph with flaps down

60 mph with 40 ( flaps (55 mph crossing the threshold) for a short field landing in smooth air

# UPPER AIR WORK

Gross weight 1600 lb – stalls, loops, spins, rolls, snap rolls, immelmanns, steep turns, lazy eights and chandelles.

# STALLING SPEEDS

Power off @ 1600 lb: Clean – 55 mph, Flaps 20 ( - 49 mph, Flaps 40( - 48 mph Steep gliding turns – 63 mph

# GLIDE

At 70 MPH the aircraft will glide 2.92 Nm from 2 000’ agl.

# SUCTION

3 – 5 inches of mercury	www.gridline.co.uk		22-Oct-00 G-BACP.doc