G-BEMB F 172M 1976

# TAKE OFF AND CLIMB

Lift nose wheel at 55 KIAS	Vy = 78 KIAS	Normal takeoff

Lift nose wheel at 55 KIAS	Climb at 59 KIAS	Short field takeoff with flaps up

Soft field use 10 ( flap		Normal climb 70 - 80 KIAS.

# FUEL

75% power, 8.2 USGPH @ 2550 RPM @ 2000’ with mixture leaned gives 116 KTAS.

65% power, 7.1 USGPH @ 2400 RPM @ 2000’ with mixture leaned gives 110 KTAS

Usable fuel is 38 US Gallons.

Aircraft weighs 1467 lb; full fuel weighs 228 lb, leaving 605 lb for crew, passengers and baggage.

# APPROACH SPEEDS

60 - 70 KIAS with flaps up, 55 - 65 KIAS with flaps down

60 KIAS with 40( of flap for a short field landing in smooth air

# UPPER AIR WORK

Utility category - 2 000 lbs:	Stalls, spins, steep turns, lazy eights and chandelles.

# STALLING SPEEDS

Power off @ 2 300 lbs:	Clean – 42 KIAS, Flaps 10( - 38 KIAS, Flaps 40( - 36 KIAS

# GLIDE

At 65 KIAS the aircraft will glide 2.5 to 3.33 nautical miles from 2 000’ agl.

# SUCTION

4.6 – 5.4 inches of mercury   	www.gridline.co.uk       22-Oct-00    G-BEMB.doc